Benchmark to choose threshold for filtering features based on variance

Low-variance features do not add much important information to the ML model to predict abiotic factors from genomic features. Therefore we will filter them out. To choose an appropriate threshold for filtering features based on their variance, we did a benchmark. This benchmark measures the model’s metrics for different thresholds. The threshold with the highest metric is chosen per abiotic factor and feature (gene families or kmers). Metrics were: F1 score and MAE (maximum absolute error) for classification and regression respectively.

First, variance was measured for each feature (gene families and kmers), using numpy function var: https://numpy.org/doc/stable/reference/generated/numpy.var.html. This function measures the spread of a distribution following the formula (sum of a minus the mean squared divided by the number of elements):

N = len(a)
d2 = abs(a - mean)**2
var = d2.sum() / (N - ddof)
Afterwards, variances were normalized to a range [0; 1] to make different features comparable following:

( variances – variances.min() ) / ( variances.max() – variances.min() )

A plot was made to understand the variances of different features. Based on the plot, we chose appropriate ranges of study for different features. The idea was to cover most of the data.

The benchmark was done with 80% of the data (training set). 20% of the data (test set) was set aside for final evaluation after feature selection and hyperparameter tuning (source: https://scikit-learn.org/stable/modules/cross_validation.html). The training and test sets were created with a reproducible command (sklearn, model_selection, train_test_split, random_state = 99).

Discussion of results

- Gene families have higher variance compared to kmers;

- For classification, salinity has a clear lower F1-score, 0.85, than temperature and oxygen, >0.96. This is not due to the lower number of samples used in the analysis, since salinity, n = 746, has more samples than temperature, n = 534 (oxygen has n = 2,722);

- For classification, the metrics do not change very much with different variance thresholds;

Normalized variances of gene families and kmer9

Conclusions:
- gene families have higher variance compared to kmers;
- for gene families, I we did the benchmark iteration between 0 and 0.01 normalized variance;
- for kmers, I we did the benchmark between 0 and 0.002 normalized variance.

Understanding normalized variances of gene families

COGs with norm_var = 0 are absent from all species in the dataframe:

How about COGs with low, non-zero variances? They are present in very few species in the dataframes ( < 0.25% os isolates).

The tables below show counts of 1s (presence) in the abiotic factor’s dataframe for the indicated filter. For normalized variances between 0.002 and 0.010, the vast majority of species do not have the COGs.

Salinity (n = 3,418):
Low-variance filter	0.002	0.003	0.004	0.005	0.006	0.008	0.009	0.010
Counts of 1s	1	2	3	4	5	6	7	8
Percentages	0.029	0.059	0.088	0.117	0.146	0.176	0.205	0.234

Temperature (n = 13,198):
Low-variance filter	0.002	0.003	0.004	0.005	0.006	0.008	0.009	0.010
Counts of 1s	4	7	10	14	17	25	27	33
Percentages	0.030	0.053	0.076	0.106	0.129	0.189	0.205	0.250

Oxygen (n = 7,255):
Low-variance filter	0.002	0.003	0.004	0.005	0.006	0.008	0.009	0.010
Counts of 1s	2	4	6	8	10	13	15	18
Percentages	0.028	0.055	0.083	0.110	0.138	0.179	0.207	0.248

pH (n = 3,630):
Low-variance filter	0.002	0.003	0.004	0.005	0.006	0.008	0.009	0.010
Counts of 1s	1	2	3	4	5	7	8	9
Percentages	0.028	0.055	0.083	0.110	0.138	0.193	0.220	0.248

How about the top 50 most important features for salinity classification? In this experiment, I built a model to classify the salinity of prokaryotic isolates based on their COG profile.

- top 50 COGs of the SVC model had normalized variance between 0.34 and 1 (possible range: [0; 1])
- top 50 COGs of the RF model had normalized variance between 0.063 and 1 (possible range: [0; 1]).

Lowest variances:
- COG1025@2 has norm var = 0.34 (lowest variance of RF) and is present in 318/3,418 isolates; it is related to post-translational modification, protein turnover, and chaperones;
- COG3544@2 has norm var = 0.06 (lowest variance of SVC) and is present in 55/3,418 isolates; it is a domain of unknown function.

RF top 50 features:	SVC top 50 features:
Feature	Norm. variance		Feature	Norm. Variance
COG1025@2	0.338		COG3544@2	0.063
COG0787@1	0.363		COG3410@1	0.136
COG3887@2	0.485		COG5617@2	0.192
COG0769@1	0.511		COG4988@1	0.306
COG1154@2	0.526		COG0173@2	0.316
COG0826@2	0.567		COG0318@1	0.345
COG0569@1	0.587		COG0532@2	0.373
COG3975@2	0.592		COG0322@2	0.417
COG1115@2	0.631		COG0129@2	0.475
COG2509@2	0.659		COG3887@2	0.485
COG3968@2	0.664		COG1154@2	0.526
COG0471@2	0.701		COG0826@2	0.567
COG1042@1	0.717		COG0569@1	0.587
COG2176@2	0.732		COG1012@2	0.654
COG0025@2	0.732		COG2509@2	0.659
COG2060@2	0.758		COG1960@2	0.660
COG2759@2	0.785		COG3968@2	0.664
COG1274@2	0.807		COG3533@2	0.671
COG3605@2	0.808		COG3347@1	0.739
COG3158@2	0.824		COG0249@2	0.748
COG4666@2	0.831		COG3285@1	0.786
COG1884@1	0.852		COG1074@2	0.797
COG5000@2	0.870		COG1033@2	0.803
COG3408@2	0.888		COG1274@2	0.807
COG2216@2	0.900		COG3605@2	0.808
COG0745@1	0.905		COG3158@2	0.824
COG0659@2	0.922		COG4666@2	0.831
COG3387@2	0.926		COG0318@2	0.838
COG2373@2	0.934		COG2866@2	0.843
COG0477@2	0.939		COG0442@2	0.860
COG0370@2	0.948		COG0358@2	0.867
COG1292@2	0.956		COG4191@1	0.878
COG3696@2	0.958		COG3408@2	0.888
COG1009@2	0.960		COG1271@2	0.896
COG1038@2	0.960		COG2216@2	0.900
COG2352@2	0.970		COG1003@1	0.924
COG0281@1	0.982		COG2373@2	0.934
COG3808@2	0.982		COG0477@2	0.939
COG0326@2	0.983		COG1292@2	0.956
COG0539@2	0.986		COG3696@2	0.958
COG2111@1	0.986		COG5002@2	0.959
COG0531@2	0.987		COG2303@2	0.960
COG1866@2	0.989		COG1554@2	0.963
COG1034@2	0.990		COG0591@2	0.968
COG0554@2	0.991		COG2902@2	0.976
COG4147@2	0.996		COG0281@1	0.982
COG0422@2	0.997		COG2838@2	0.983
COG1032@2	0.998		COG0753@2	0.994
COG1523@2	1.000		COG1032@2	0.998
COG0277@1	1.000		COG1523@2	1.000

Salt, gene-families

Classification (RF, undersampling)	Regression (RF, mean NaCl)
Number of initial isolates for filtering: 3,418	Number of initial isolates for filtering: 3,418
Number of initial features: 20,141	Number of initial features: 20,141
Number of isolates considered in the analysis: 746	Number of isolates of analysis: 2,734

Choice of threshold: 0.009	Choice of threshold: 0.001
Obs: The numbers on top of the plot indicate the percentage of features that are filtered out when applying the filtering, “all” indicates no filter was applied.

Of the initial 20,141 Gfs, 9,155 (45.5%) had zero normalized variance. All of the 9,155 COGs had zeroes in the dataframe.

Salt, kmer9

Classification (RF, undersampling)	Regression (RF, mean NaCl)
Number of initial isolates for filtering: 3,418	Number of initial isolates for filtering: 3,418
Number of initial features: 131,072	Number of initial features: 131,072
Number of isolates considered in the analysis: 746	Number of isolates of analysis: 2,734

Choice of threshold: 0.001	Choice of threshold: 0.0014

Temperature, gene-families

Classification (RF, undersampling)	Regression (RF, mean temperature)
Number of initial isolates for filtering: 13,198	Number of initial isolates for filtering: 13,198
Number of initial features: 20,141	Number of initial features: 20,141
Number of isolates considered in the analysis: 534	Number of isolates considered in the analysis: 10,558

Choice of threshold: 0.009	Choice of threshold: 0.005
Obs: Mann-Whitney test p-value > 0.05 for groups marked in orange and red. This means that “no filter” and filtering features with 0.0 variance have no difference in the RF metrics. Additionally, some other groups also have no difference in the RF metrics.

Temperature, kmer9

Classification (RF, undersampling)	Regression (RF, mean NaCl)
Number of initial isolates for filtering: 13,198	Number of initial isolates for filtering: 13,198
Number of initial features: 131,072	Number of initial features: 131,072
Number of isolates considered in the analysis: 534	Number of isolates considered in the analysis: 10,558

Choice of threshold: 0.0	Choice of threshold: 0.0002

Oxygen, classification

Gene families (RF, undersampling)	kmer9 (RF, undersampling)
Number of initial isolates for filtering: 7,255	Number of initial isolates for filtering: 7,255
Number of initial features: 20,141	Number of initial features: 131,072
Number of isolates considered in the analysis: 2,722	Number of isolates considered in the analysis: 2,722

Choice of threshold: 0.009	Choice of threshold: 0.0002

pH, regression

Gene families (RF, mean pH)	kmer9 (RF, mean pH)
Number of initial isolates for filtering: 3,630	Number of initial isolates for filtering: 3,630
Number of initial features: 20,141	Number of initial features: 131,072
Number of isolates considered in the analysis: 2,904	Number of isolates considered in the analysis: 2,904

Choice of threshold: 0.010	Choice of threshold: 0.0008